JHM DTS Allroad Adapter kit

Contents of package

- 2 – Allroad specific Aluminum spacers (to go between the DTS and the body of the car)

- 4 - 8mm hex bolts, 55mm long (to replace the 8mm flange hex bolts that come in the kit)

- 4 - 8mm washers (to go between the 55mm bolts and the DTS itself)

Required tools

Cut-off tool or dremel tool.

Installation

Make sure you read all the instructions from the JHM DTS kit and then use this only as a supplement for the installation of the adapters with the DTS kit.  This adapter kit fills the space between the DTS and the body on the Allroad to make it a perfect fit. It also requires some clearancing of the off-road gaurd on the factory drivers side downpipe near the flex coupler.  The DTS will not clear this unless you cut the excess off of the factory downpipes, once removed there is still enough material for offroad protection and the DTS would aid in this as well.  So you have nothing to worry about if you take your Allroad off-road.

- You can see in this pic where the factory drivers side guard needs to be cut.  You will remove about .3” a little over a ¼” to make room for the JHM DTS.

- You will now install the DTS as per the original instructions except you will add the 2 included spacers between the DTS and body while also using the included longer bolts and washers as well.  You need to make sure the recess in the adapter slips into the end of the DTS. See pic below.